## Slide 1: Welcome to EMK310 continued…

## Slide 2: Assistant Lecturers
AGS - Mr Alkmaar Swart
Race Day - Mr Bernard Bauermeister
Pracs - Mr Duayne Strydom
Theory - Mr Jacques Van der Westhuizen
General – Ms Elizabeth Stanley

## Slide 3: Practicals: Hardware
PICkit 3 included in tuition fees
Microchip samples (sponsored by Microchip)
N20-kit brushed dc motor included in tuition fees (compulsory motor for ARV)
Collection of PICkit3, motor & sponsored components
  Refer to ClickUp page for date and time
  Must be registered for the module
  Bring along anti-static packaging for the samples (e.g. a piece of polystyrene covered with foil)
Collect on Friday

## Slide 4: Test and exams
Semester tests
  First: Theory
    Multiple choice
  Second: Application
    Coding in computer lab; upload code onto server.
    Open book. Refer to study guide.
    100% penalization if code does not compile.
    Automatic grading
Class tests
  First: Application
    Same rules apply as for semester test 2
  Second: Theory
    Same rules apply as for semester test 1
Exam
  Theory and coding
    Open book. Refer to study guide.
    In computer lab
    100% penalization if code does not compile.
    Automatic grading
Semester test 1 & Class test 2
(Theory)

## Slide 5: Automatic grading software (AGS)
Objective
Subsections of code
Strict syntax requirements
Immediate results
Binary marking for subsections (as was the case since always)
Opportunity for practice via old tests and exams
  (this means you'll never get an old paper, so don't memorize old memos)

## Slide 6: AGS panel
Objective: optimization of AGS for variations in interpretation and implementation.
Members: good students appointed by class through class reps
  3 Electronic
  3 Electrical
  4 Computer
Responsibilities: All coding tests graded
  by AGS including sick & supp.
Approach: Panel’s code will be put through AGS first, AGS is then optimized after which bulk of tests are graded.
  Tested in 2014 > extremely effective.
Please…

## Slide 7: Subminima
Semester mark (Exam entrance)
  40% for pracs
  40% for theory (textbook) component
  40% for application (code) component
Examination
  40% for theory (textbook) component
  40% for application (code) component

## Slide 8: Schedule
Complete schedule, including class tests, practical tutor sessions, additional lectures, practical demonstrations, etc. is given on the module’s ClickUp site.
Under development to (i) align with ENE310 and (ii) disrupt-proof the module.

## Slide 9: What do I do in my EMK time?
Bioengineering!
Cochlear Implants

## Slide 10: What is a cochlear implant?
Sound processor
Transcutaneous telemetry coil for power and data transfer
Implanted electronics and electrode array
Hearing nerve

## Slide 11: Why do cochlear implants work?
Nerve fibres are electrically excitable
Tonotopic organization of nerve fibres
Neural excitation dictated by electrode-nerve fibre interface

## Slide 12: Generation of user-specific models

## Slide 13: User-specific models

## Slide 14
Opportunities
Our research group is internationally recognised and respected.
We publish our research in leading international journals.
If you are interested to apply your engineering skills to solve problems in neuroscience, perception, music perception, cochlear implants or psychoacoustics, postgraduate studies in the bioengineering group are for you!
Talk to me or Prof Johan Hanekom about opportunities for full-time postgraduate study.

## Slide 15: EMK310 Lecture 1 Introduction to Microcontrollers & PIC Theory & Application Professor Tania Hanekom tania.hanekom@up.ac.za Copyright reserved by University of Pretoria
References:
Bolton chapter 1
Projects.pdf
PIC18 datasheet & reference manual
Your own background reading in other relevant sources

## Slide 16: SO WHAT IS A μP OR A μC?
Before we start on the car, we need to have a little background…

## Slide 17: A microprocessor is a…
digital device that
accepts data from a number of input lines
processes the data according to software in the micro
produces a number of output signals
and has inputs and outputs
discrete on/off signal from sensor or other device, i.e. 1 or 0
parallel group to represent binary number, e.g. 10110010

## Slide 18: Microcontroller vs microprocessor
A microcontroller consistes of
a microprocessor, i.e. CPU
onboard memory, and
onboard peripherals, e.g. ADC, PWM, etc.

## Slide 19: Where do microprocessors come from and where do we use them?
Became commercially available in 1971
  4 bit Intel 4004
    4 bit micros still used today for simple applications
  1980s came 8 bit micros
  4  8  16  32  64 bit microprocessors
Today they are being used in…
  … and as the controller for our ARV.

PCs

Desktop
microcomputers

## Slide 20: "OUR" micros
PIC18F45K20 (95% of module's focus)
PIC32MX220F032 (5% of module's focus)

## Slide 21: Micros can’t think…
…so you have to tell them exactly what to do.
Programs (software)
  set of instructions stored in computer's memory
  machine instructions coded as binary numbers
Instruction are
  fetched from memory
  decoded in control unit of CPU…
  which generates control signals to trigger operation

## Slide 22: Data representation in micros
Digital system signals in one of two states: 0 or 1
Binary digits = bits
Bits represented by voltage levels
  Logic 1 = 5 V (ideal)
  Logic 0 = 0 V (ideal)
  TTL (transistor-transistor logic)
    Inputs Low 0 to 0.8 V High 2.0 to 5.0 V
    Outputs Low 0 to 1.5 V High 3.5 to 5.0 V
  CMOS (complementary metal oxide semiconductors)
    Inputs Low 0 to 1.5 V High 3.5 to 5.0 V
    Outputs Low 0 V High 5.0 V

## Slide 23: Assembly language
Programmer needs to enter instructions, debug and maintain code
using binary format
  e.g. 0000 1000 0000 0011 (Not likely!)
or in hex
  0803h (Still doesn't mean anything to the novice.)
or perhaps
  movf 03h, 0 (Looks a tiny bit better. Maybe move something?)
or how about
  movf STATUS, W
  meaning "Move the contents of a file register called Status into a register called W."
  Yes, much better if we know what "STATUS" and "W" means!

## Slide 24: Assembly language (2)
Assembly language
  was developed to simplify the programming job.
  is a low-level programming language which is used to manipulate microcontroller on bit and word level.
How does it get into the μ?
  Source code: the code we write
    instructions: PIC understands them
    directives: control how the assembler builds the object code (see MPLAB help)
  Assembled to hex file (object code) by assembler software
    Assembler must understand each line of code to be able to do the translation

## Slide 25: High-level languages
To code in Assembler, the programmer must know hardware architecture of micro on which software is to be executed
  (This is exactly why we program in Assembler in EMK310)
High-level languages require less knowledge of underlying hardware and the code is easier to follow. However,…
  machine code compiled from high-level language is much longer and cannot run as fast as equivalent Assembler code.
  time-critical applications frequently written in Assembler.

## Slide 26: Number systems (ERS220)
Selfstudy
  Binary
  Octal
  Hexadecimal
  BCD
  Binary arithmetic
  Floating points
  ASCII

## Slide 27: Architecture

## Slide 28: Architecture
What is "microcontroller architecture"?
  What microcontrollers look like and the principles on which it operates.
  The term includes a description of
    the type of instruction set,
    the memory structure,
    the hardware setup,
    how instructions are executed (pipelined or not),
    word size.

## Slide 29: Microprocessor systems
Components
  Central processing unit (CPU)
  Memory to store data & instructions
  Input/output interfaces (ports)
Digital signals move from one component to another along three buses
  Data bus
  Address bus
  Control bus

## Slide 30: Architecture: Hardware setup
Microcontroller consists of
CPU modules
  Arithmetic and logic unit (ALU)
    Afrikaans: rekenkundige-en-logiese-bewerkingseenheid
    8 bit on the 8 bit PICs
  Registers
  Control unit [beheereenheid]
Other devices
  Separate memories to store program & data
  Oscillator & timers
  Interfaces, e.g. ports, ADC, comparators, PWM
External control signals
CPU Architecture

## Slide 31: Architecture
PIC18F45K20
datasheet p. 15
Clock & timing unit
ALU
I/O Ports
Timers

## Slide 32: PIC10F200
datasheet p. 10
6 pin!

## Slide 33: PIC32MX220F032B
PIC32 family reference manual

## Slide 34: MEMORY

## Slide 35: Memory
Memory location (information unit)
  Address & content
0 1 0 0 1 0 0 1
03h

## Slide 36: Memory
Microcontrollers have data memory and program memory.
  Data memory is used to store numbers that you are working with.
  Program memory is where the program, consisting of instructions, is stored.

## Slide 37: Architecture: Memory structure
Harvard architecture
  program & data accessed from separate memories via separate busses
  word width, timing, implementation technology, and memory address structure can differ
  instruction memory often wider than data memory
  advantage: bandwidth, i.e. much faster
  vs Von Neumann architecture…

## Slide 38: Word sizes
A word is a collection of bits that are required to represent data or address
  e.g. if 10 bits are used to represent address in micro, it uses a 10 bit address word
  e.g. if 8 bits are used to represent data in micro, it uses an 8 bit data word
There is frequently (mostly) a difference between the address word size and the data word size in a microprocessor.

## Slide 39: Word sizes (2)
The PIC18F45K20 has a(n)
8-bit wide data path – remember: microprocessors are classified according to size of data bus/data word, i.e. 8 bit micro has an 8 bit data bus/word
16-bit wide instruction set.

## Slide 40: Memory maps
Provides a "map" to show which addresses are used for which microprocessor element

## Slide 41: Types of memory
Two very general types of memory
  on-chip
  external (e.g., I2C EEPROM of Prac 2)
On-chip memory
Can be divided into
  program memory (instruction code)
  data memory (variables)
For PIC processors the two blocks of memory each has its own bus
  access to each in same oscillator cycle

## Slide 42: Program memory
21-bit program counter, capable of addressing 2 MB program memory space
  (221 = 2 097 152)
32 Kbytes of Flash Memory implemented on PIC18F45K20
  8000h = 32 768d
  up to 16,384 single-word instructions (remember, one instruction word is 2 bytes wide)

## Slide 43: Data memory
Data memory consists of
Special Function Registers (SFR)
  control the operation of the device
General Purpose Registers (GPR)
  general area for data storage and scratch pad operations.

## Slide 44: Communication inside the microcontroller

## Slide 45: Standard buses
Address bus
Data bus
Control bus
Chip select / enable
Clock
Ports

## Slide 46: Data bus
A bus is a "collection of wires" through which communication occurs
Carries data that needs to be processed
Tristate output interfaces to prevent devices that are not in use to provide low impedance current path that could prevent correct logic levels at device being addressed
Three states: high signal, low signal & high impedance

## Slide 47: Data bus (continued)
Width of the data path/bus
  determines the number of input lines on which data can enter the microprocessor
Data bus
  lines carrying the data
  electrical conductors, i.e. hardware implementation

## Slide 48: Data bus (continued)
Microprocessors are classified according to size of data bus/data word
  i.e. 8 bit micro has an 8 bit data bus/word
  LSB is bit 0
  MSB is bit 7
Note:
  8 bits = byte (always)
  4 bits = nibble (always)

## Slide 49: Zero condition 1
An 8 bit micro's data are stored in 8 bit registers
If you pass a 16 bit binary number in your code to an 8 bit data register, what happens to the most significant 8 bits?
Will your program work?
If you do this in a test or exam, you get 0 for the entire test or exam.
Same fundamental principle as that 2 litres of water cannot fit into a 1 litre container…
Register
Data bits
0
7

## Slide 50: Address bus
Each storage location (register) in a memory device has an address so that system can locate instructions or data in memory.
Each input/output interface has an address too.
Only the device/memory location whose address is placed on the address bus is enabled for communication.
Address decoder is used when there are many devices to be addressed
  Output of address decoder activates the device via its chip select (CS) input.

## Slide 51: Control bus
Carries control signals e.g. read/write & clock signals
READ/WRITE line
  1 on line = read (receive a signal)
  0 on line = write (send a signal)
Clock
  Signal to synchronise microprocessor functions
  External or internal

## Slide 52: Signal conditions on lines or buses
Invalid data
  signal transition
  Shows how long a transition takes
Bit signal level shown with line
Bus signal levels shown with bar

## Slide 53: Timing diagrams to show sequence of events on lines, buses and inside registers
T-state = 1 clock cycle = T
Machine cycle = number of clock cycles required to complete a basic operation (e.g. fetch, read or write) x T
Instruction cycle = number of clock cycles required to complete
an instruction x T
Timing diagrams are used to show the chronological sequence of events or signals in a digital system

## Slide 54: INSTRUCTIONS

## Slide 55: Architecture: Instruction set
RISC
reduced instruction set computer
simplified instructions which "do less" may still provide for higher performance if this simplicity can be utilized to make instructions execute very fast
PICs are RISK machines
vs CISC (complex instruction set computer…)

## Slide 56: Architecture: execution of instructions
Fetch-execute cycle
Fetch operator code (instruction) from memory & store in instruction register
Decode instruction in instruction decoder
Fetch further data if required
Execute the instruction
Goto 1.

## Slide 57: READY TO GO…

## Slide 58: Flashing an LED = “Hello World”
What do we need?
  power to power the μ
  clock source required for processing
  code to tell the PIC what to do
  LED and resistor to limit current through LED
    port pins can source/sink 25 mA but it is better design practice to use a resistor

## Slide 59: But…
PICs understand only 0 and 1 because they are made of transistors (switches)
we don't think in terms of 0 and 1 (maybe students do the day or two after RAG…)

## Slide 60: What to do?
We decided that none of the following techniques are suitable for programming at this stage:
  Binary machine code (e.g. 0111001010001010)
  Hex (e.g. 0803h)
  Assembler using only numbers in the operant fields (e.g. movf 03h, 0)
We'll rather use instructions with register names that are more understandable
  movf STATUS, W

## Slide 61: Mnemonics
Interface between student and microcontroller
An assembler is used to translate the code written using mnemonics (that we understand easier) to machine code (the micro’s language)
  some people learn to understand machine code as if it were English!

## Slide 62: Example of Assembler code
Label Mnemonic Operand Comments
Instruction
Directive
Title "Our first program" (directive)
list p=pic18f45k20 ; processor type (directive)
;
; ------------- (comment)
; PROGRAM START (comment)
; ------------- (comment)
;
org 0h ; startup address = 0000 (directive)
start movlw 0x00 ; simple code (instruction)
movwf 0F80h (instruction)
goto start ; do this loop forever (instruction)
end (directive)
projects.pdf p. 16

## Slide 63: Agenda: Coding lecture (next week)
MPLAB X demo
  new project;
  editing code;
  compile;
  debugger & MPLAB sim;
  run (watchdog timer timeout);
  configuration bits (explain + not accessible after PIC has been programmed);
  oscillator;
  watchdog (reset PIC after some predefined time);
  power up timer.

## Slide 64: Homework
Form teams
Work through Prac assignment
Start on planning documentation
What do you want to learn next week? Class reps?