## Slide 1: Function Head: Undergraduate
My role as head of undergrad studies
Where are we now and where are we heading?
  Bloom's taxonomy
What are your expectations?
How is the Department doing?
EECE Undergrad website? Nice or not?
Feedback: Class reps
Strategy:
  Mainly email to
    help you to express your situation
    help you to express your request
    help me to help you ASAP
  Meeting if issue cannot be resolved via email.

## Slide 2: EPY423
Vacation work and report module usually taken in 4th year
20 x 8-hour days (absolute minimum)
Proper vacation work opportunities for June/July recess may be available through community service office of UP
  Ms Gernia van Niekerk
  You must also try to arrange your own vacation work
Register for placement via EECE Undergraduate ClickUP when it becomes available.
Report will be fill-in on EPY ClickUp website – available as soon as you register for the module.
Department of Electrical, Electronic and Computer Engineering

## Slide 3: Welcome to EMK310 continued…

## Slide 4: Assistant Lecturers
AGS - Mr Tinus Green
Race Day - Mr Jaco Marais
Pracs - Mr Duayne Strydom
Theory - Mr Jacques Van der Westhuizen
CTS/General - Mr Bernard Bauermeister

## Slide 5: Practicals: Broad assignment
The 4th annual EMK 310 RACE DAY will take place on 23 May 2016
Design, construct & test a microcontroller-based autonomous robotic vehicle (ARV) from first principles.
ARV navigates by following a coloured line on a light surface.
The objective is to accurately follow a track in the fastest possible time from start to finish.
A PIC18F45K20 must be used as the processor platform.
All code must be developed in Assembly Language.
The chassis and other structural components required to construct the robotic vehicle must be made from recycled materials and/or the chassis may be designed by your team and printed on a 3D printer.
A group's ARV must take part in the 4th annual EMK 310 Race Day for group members to be eligible to write the exam.

## Slide 6: Practicals: Hardware
PICkit 3 included in tuition fees
Microchip samples (sponsored by Microchip)
N20-kit brushed dc motor included in tuition fees (compulsory motor for ARV)
Collection of PICkit3, motor & sponsored components
  Refer to ClickUp page for date and time
  Must be registered for the module
  Bring along anti-static packaging for the samples (e.g. a piece of polystyrene covered with foil)

## Slide 7: Test and exams
Semester tests
  First: Theory
    Multiple choice
  Second: Application
    Coding in computer lab; upload code onto server.
    Open book. Refer to study guide.
    100% penalization if code does not compile.
    Automatic grading
Class tests
  First: Application
    Same rules apply as for semester test 2
  Second: Theory
    Same rules apply as for semester test 1
Exam
  Theory and coding
    Open book. Refer to study guide.
    In computer lab
    100% penalization if code does not compile.
    Automatic grading
Semester test 1 & Class test 2
(Theory)

## Slide 8: Automatic grading software (AGS)
Objective
Subsections of code
Strict syntax requirements
Immediate results
Binary marking for subsections (as was the case since always)
Opportunity for practice via old tests and exams
  (this means you'll never get an old paper, so don't memorize old memos)

## Slide 9: AGS panel
Objective: optimization of AGS for variations in interpretation and implementation.
Members: good students appointed by class through class reps
  3 Electronic
  3 Electrical
  4 Computer
Responsibilities: All coding tests graded
  by AGS including sick & supp.
Approach: Panel’s code will be put through AGS first, AGS is then optimized after which bulk of tests are graded.
  Tested in 2014 > extremely effective.
Please…

## Slide 10: Subminima
Semester mark (Exam entrance)
  40% for pracs
  40% for theory (textbook) component
  40% for application (code) component
Examination
  40% for theory (textbook) component
  40% for application (code) component

## Slide 11: Schedule
Complete schedule, including class tests, practical tutor sessions, additional lectures, practical demonstrations, etc. is given on the module’s ClickUp site.
Under development to align with ENE310.

## Slide 12: What do I do in my EMK time?
Bioengineering!
Cochlear Implants

## Slide 13: What is a cochlear implant?
Sound processor
Transcutaneous telemetry coil for power and data transfer
Implanted electronics and electrode array
Hearing nerve

## Slide 14: Why do cochlear implants work?
Nerve fibres are electrically excitable
Tonotopic organization of nerve fibres
Neural excitation dictated by electrode-nerve fibre interface

## Slide 15: Some present research topics
User-specific models
Acoustic models
Perception models

## Slide 16: Computational physiology: modelling of the electrode-nerve interface
Finite element model of
human cochlea, v 1.0
2001
Finite element model of
human cochlea, v 2.0
2013

## Slide 17: Guinea-pig model
FE model with surrounding
bone omitted
Potential distribution predicted as
a result of intracochlear stimulation

## Slide 18: Basic form of neural models

## Slide 19: Generation of user-specific models

## Slide 20: User-specific models

## Slide 21
Opportunities
Our research group is internationally recognised and respected.
We publish our research in leading international journals.
If you are interested to apply your engineering skills to solve problems in neuroscience, perception, music perception, cochlear implants or psychoacoustics, postgraduate studies in the bioengineering group are for you!
Talk to me or Prof Johan Hanekom about opportunities for full-time postgraduate study.

## Slide 22: EMK310 Lecture 1 Introduction to Microcontrollers & PIC Theory & Application Professor Tania Hanekom tania.hanekom@up.ac.za Copyright reserved by University of Pretoria
References:
Bolton chapter 1
Projects.pdf
PIC18 datasheet & reference manual
Your own background reading in other relevant sources

## Slide 23: SO WHAT IS A μP OR A μC?

## Slide 24: A microprocessor is a…
digital device that
accepts data from a number of input lines
processes the data according to software in the micro
produces a number of output signals
and has inputs and outputs
discrete on/off signal from sensor or other device, i.e. 1 or 0
parallel group to represent binary number, e.g. 10110010

## Slide 25: Microcontroller vs microprocessor
A microcontroller consistes of
a microprocessor, i.e. CPU
onboard memory, and
onboard peripherals, e.g. ADC, PWM, etc.

## Slide 26: Where do microprocessors come from and where do we use them?
Became commercially available in 1971
  4 bit Intel 4004
    4 bit micros still used today for simple applications
  1980s came 8 bit micros
  4  8  16  32  64 bit microprocessors
Today they are being used in…
  … and as the controller for our ARV.

PCs

Desktop
microcomputers

## Slide 27: "OUR" micros
PIC18F45K20 (95% of module's focus)
PIC32MX220F032 (5% of module's focus)
https://kahoot.it/
(40 minutes)

## Slide 28: Micros can’t think…
…so you have to tell them exactly what to do.
Programs (software)
  set of instructions stored in computer's memory
  machine instructions coded as binary numbers
Instruction are
  fetched from memory
  decoded in control unit of CPU…
  which generates control signals to trigger operation

## Slide 29: Data representation in micros
Digital system signals in one of two states: 0 or 1
Binary digits = bits
Bits represented by voltage levels
  Logic 1 = 5 V (ideal)
  Logic 0 = 0 V (ideal)
  TTL (transistor-transistor logic)
    Inputs Low 0 to 0.8 V High 2.0 to 5.0 V
    Outputs Low 0 to 1.5 V High 3.5 to 5.0 V
  CMOS (complementary metal oxide semiconductors)
    Inputs Low 0 to 1.5 V High 3.5 to 5.0 V
    Outputs Low 0 V High 5.0 V

## Slide 30: Assembly language
Programmer needs to enter instructions, debug and maintain code
using binary format
  e.g. 0000 1000 0000 0011 (Not likely!)
or in hex
  0803h (Still doesn't mean anything to the novice.)
or perhaps
  movf 03h, 0 (Looks a tiny bit better. Maybe move something?)
or how about
  movf STATUS, W
  meaning "Move the contents of a file register called Status into a register called W."
  Yes, much better if we know what "STATUS" and "W" means!

## Slide 31: Assembly language (2)
Assembly language
  was developed to simplify the programming job.
  is a low-level programming language which is used to manipulate microcontroller on bit and word level.
How does it get into the μ?
  Source code: the code we write
    instructions: PIC understands them
    directives: control how the assembler builds the object code (see MPLAB help)
  Assembled to hex file (object code) by assembler software
    Assembler must understand each line of code to be able to do the translation

## Slide 32: High-level languages
To code in Assembler, the programmer must know hardware architecture of micro on which software is to be executed
  (This is exactly why we program in Assembler in EMK310)
High-level languages require less knowledge of underlying hardware and the code is easier to follow. However,…
  machine code compiled from high-level language is much longer and cannot run as fast as equivalent Assembler code.
  time-critical applications frequently written in Assembler.

## Slide 33: Number systems
Selfstudy
  Binary
  Octal
  Hexadecimal
  BCD
  Binary arithmetic
  Floating points
  ASCII

## Slide 34: Architecture

## Slide 35: Architecture
What is "microcontroller architecture"?
  What microcontrollers look like and the principles on which it operates.
  The term includes a description of
    the type of instruction set,
    the memory structure,
    the hardware setup,
    how instructions are executed (pipelined or not),
    word size.

## Slide 36: Microprocessor systems
Components
  Central processing unit (CPU)
  Memory to store data & instructions
  Input/output interfaces (ports)
Digital signals move from one component to another along three buses
  Data bus
  Address bus
  Control bus

## Slide 37: Architecture: Hardware setup
Microcontroller consists of
CPU modules
  Arithmetic and logic unit (ALU)
    Afrikaans: rekenkundige-en-logiese-bewerkingseenheid
    8 bit on the 8 bit PICs
  Registers
  Control unit [beheereenheid]
Other devices
  Separate memories to store program & data
  Oscillator & timers
  Interfaces, e.g. ports, ADC, comparators, PWM
External control signals
CPU Architecture

## Slide 38: Architecture
PIC18F45K20
datasheet p. 15
Clock & timing unit
ALU
I/O Ports
Timers

## Slide 39: PIC10F200
datasheet p. 10
6 pin!

## Slide 40: PIC32MX220F032B
PIC32 family reference manual

## Slide 41: MEMORY

## Slide 42: Memory
Memory location (information unit)
  Address & content
0 1 0 0 1 0 0 1
03h

## Slide 43: Memory
Microcontrollers have data memory and program memory.
  Data memory is used to store numbers that you are working with.
  Program memory is where the program, consisting of instructions, is stored.

## Slide 44: Architecture: Memory structure
Harvard architecture
  program & data accessed from separate memories via separate busses
  word width, timing, implementation technology, and memory address structure can differ
  instruction memory often wider than data memory
  advantage: bandwidth, i.e. much faster
  vs Von Neumann architecture…

## Slide 45: Word sizes
A word is a collection of bits that are required to represent data or address
  e.g. if 10 bits are used to represent address in micro, it uses a 10 bit address word
  e.g. if 8 bits are used to represent data in micro, it uses an 8 bit data word
There is frequently (mostly) a difference between the address word size and the data word size in a microprocessor.

## Slide 46: Word sizes (2)
The PIC18F45K20 has a(n)
8-bit wide data path – remember: microprocessors are classified according to size of data bus/data word, i.e. 8 bit micro has an 8 bit data bus/word
16-bit wide instruction set.

## Slide 47: Memory maps
Provides a "map" to show which addresses are used for which microprocessor element

## Slide 48: Types of memory
Two very general types of memory
  on-chip
  external (e.g., I2C EEPROM of Prac 2)
On-chip memory
Can be divided into
  program memory (instruction code)
  data memory (variables)
For PIC processors the two blocks of memory each has its own bus
  access to each in same oscillator cycle

## Slide 49: Program memory
21-bit program counter, capable of addressing 2 MB program memory space
  (221 = 2 097 152)
32 Kbytes of Flash Memory implemented on PIC18F45K20
  8000h = 32 768d
  up to 16,384 single-word instructions (remember, one instruction word is 2 bytes wide)

## Slide 50: Data memory
Data memory consists of
Special Function Registers (SFR)
  control the operation of the device
General Purpose Registers (GPR)
  general area for data storage and scratch pad operations.

## Slide 51: Communication inside the microcontroller

## Slide 52: Standard buses
Address bus
Data bus
Control bus
Chip select / enable
Clock
Ports

## Slide 53: Data bus
A bus is a "collection of wires" through which communication occurs
Carries data that needs to be processed
Tristate output interfaces to prevent devices that are not in use to provide low impedance current path that could prevent correct logic levels at device being addressed
Three states: high signal, low signal & high impedance

## Slide 54: Data bus (continued)
Width of the data path/bus
  determines the number of input lines on which data can enter the microprocessor
Data bus
  lines carrying the data
  electrical conductors, i.e. hardware implementation

## Slide 55: Data bus (continued)
Microprocessors are classified according to size of data bus/data word
  i.e. 8 bit micro has an 8 bit data bus/word
  LSB is bit 0
  MSB is bit 7
Note:
  8 bits = byte (always)
  4 bits = nibble (always)

## Slide 56: Zero condition 1
An 8 bit micro's data are stored in 8 bit registers
If you pass a 16 bit binary number in your code to an 8 bit data register, what happens to the most significant 8 bits?
Will your program work?
If you do this in a test or exam, you get 0 for the entire test or exam.
Same fundamental principle as that 2 litres of water cannot fit into a 1 litre container…
Register
Data bits
0
7

## Slide 57: Address bus
Each storage location (register) in a memory device has an address so that system can locate instructions or data in memory.
Each input/output interface has an address too.
Only the device/memory location whose address is placed on the address bus is enabled for communication.
Address decoder is used when there are many devices to be addressed
  Output of address decoder activates the device via its chip select (CS) input.

## Slide 58: Control bus
Carries control signals e.g. read/write & clock signals
READ/WRITE line
  1 on line = read (receive a signal)
  0 on line = write (send a signal)
Clock
  Signal to synchronise microprocessor functions
  External or internal

## Slide 59: Signal conditions on lines or buses
Invalid data
  signal transition
  Shows how long a transition takes
Bit signal level shown with line
Bus signal levels shown with bar

## Slide 60: Timing diagrams to show sequence of events on lines, buses and inside registers
T-state = 1 clock cycle = T
Machine cycle = number of clock cycles required to complete a basic operation (e.g. fetch, read or write) x T
Instruction cycle = number of clock cycles required to complete
an instruction x T
Timing diagrams are used to show the chronological sequence of events or signals in a digital system

## Slide 61: INSTRUCTIONS

## Slide 62: Architecture: Instruction set
RISC
reduced instruction set computer
simplified instructions which "do less" may still provide for higher performance if this simplicity can be utilized to make instructions execute very fast
PICs are RISK machines
vs CISC (complex instruction set computer…)

## Slide 63: Architecture: execution of instructions
Fetch-execute cycle
Fetch operator code (instruction) from memory & store in instruction register
Decode instruction in instruction decoder
Fetch further data if required
Execute the instruction
Goto 1.

## Slide 64: READY TO GO…

## Slide 65: Flashing an LED = “Hello World”
What do we need?
  power to power the μ
  clock source required for processing
  code to tell the PIC what to do
  LED and resistor to limit current through LED
    port pins can source/sink 25 mA but it is better design practice to use a resistor

## Slide 66: But…
PICs understand only 0 and 1 because they are made of transistors (switches)
we don't think in terms of 0 and 1 (maybe students do the day or two after RAG…)

## Slide 67: What to do?
We decided that none of the following techniques are suitable for programming at this stage:
  Binary machine code (e.g. 0111001010001010)
  Hex (e.g. 0803h)
  Assembler using only numbers in the operant fields (e.g. movf 03h, 0)
We'll rather use instructions with register names that are more understandable
  movf STATUS, W

## Slide 68: Mnemonics
Interface between student and microcontroller
An assembler is used to translate the code written using mnemonics (that we understand easier) to machine code (the micro’s language)
  some people learn to understand machine code as if it were English!

## Slide 69: Example of Assembler code
Label Mnemonic Operand Comments
Instruction
Directive
Title "Our first program" (directive)
list p=pic18f45k20 ; processor type (directive)
;
; ------------- (comment)
; PROGRAM START (comment)
; ------------- (comment)
;
org 0h ; startup address = 0000 (directive)
start movlw 0x00 ; simple code (instruction)
movwf 0F80h (instruction)
goto start ; do this loop forever (instruction)
end (directive)
projects.pdf p. 16

## Slide 70: Here we go hands-on…
MPLAB X
  Microchip's Integrated Development Environment
  Used to write code (editor)
  Compile code
  Debug
  Download object code to PIC via some interface
    e.g. PICkit

## Slide 71: Agenda: Coding lecture (next week)
MPLAB X demo
  new project;
  editing code;
  compile;
  debugger & MPLAB sim;
  run (watchdog timer timeout);
  configuration bits (explain + not accessible after PIC has been programmed);
  oscillator;
  watchdog (reset PIC after some predefined time);
  power up timer.

## Slide 72: Tutorials
Details to be posted on ClickUP
2 x Theory (Jacques) + 1 x Coding (Duane)
Old test and exam papers
Tut 1 next week.